## Slide 1: Gesture controlled vehicle
By,
Sara Amendola
Puneet Chugh
Prasanth

## Slide 2: Planned Features
Gesture based control interface with hands.
Engage/dis-engage and start/stop features.
Speed control for movement.

## Slide 3: Implemented features
Remote control interface instead of wearable interface.
Push buttons and indicators with LED’s for Engage and Start functions.
Speed Control

## Slide 4: Hardware Used
Arduino Uno microcontroller boards
Xbee Communication Chips
20A dual DC motor driver
MPU-6050 6-axis gyroscope and accelerometer
LEDs, Pushbuttons and packaging material.
RC car

## Slide 5: Cost Involved
Item | Cost
Arduino Uno (2) | $40
Xbee S2 (2) and Shields | $50
20A Dual Dc Motor Driver | $12
MPU6050 | $11
Packaging and Misc. | $25
TOTAL | $138

## Slide 6: Changes
Previous idea for deriving gestures is not so user friendly.
Remote control is much better than a wearable interface in some cases.
Easier to learn and exercise.

## Slide 7: Working
Multi-loop algorithm
Threshold Division

## Slide 8
x = accel_t_gyro.value.y_accel;
x = map(x, -8000, 13000, 200, 0);
x = constrain (x,0,200);
val = accel_t_gyro.value.z_accel;
val = map(val, -15000, 15000, 0, 180);
val = constrain (val,0,180);
encodedValue = val*100000 + x ;
Serial.println(encodedValue);
while(start == 0)
{
Serial.println(disEngage);
delay(100);
if(digitalRead(6) == 1)
{
while(digitalRead(6) == 1)
{
}
start = 1;
digitalWrite(8,HIGH);
}
}
if(digitalRead(6) == 1)
{
while(digitalRead(6) == 1)
{
}
start = 0;
digitalWrite(8,LOW);
}
while(engage == 1)
{
Serial.println(encodedValue);
delay(100);
if(digitalRead(7) == 1)
{
while(digitalRead(7) == 1)
{
}
engage = 0;
digitalWrite(9,LOW);
}
}
if(digitalRead(7) == 1)
{
while(digitalRead(7) == 1)
{
}
engage = 1;
digitalWrite(9,HIGH);
}

## Slide 9: questions! Thank You