## Slide 1: SHADOW FAN
Lalit Damodaran
Mrudula Vaidya
Pratyush Bangera

## Slide 2: CONTENTS
Introduction
Goals
Construction
Circuits
Working
Problems Solved
Cost Analysis
Future Scope

## Slide 3: INTRODUCTION
Standard fans are widely used in personal office spaces.
Typically provided with 2 modes – Static and a Preset swing mode
The first mode requires physical effort for the fan to be directed to the changing position of the user
The second mode can ne wasteful as the fan may be directed to empty spaces due to preset swing.

## Slide 4: GOALS
Design an automated fan that follows the user’s movement.
Change the speed of the fan depending on the ambient temperature
In case of more than a single user, provide automated oscillation of the pan, based on their positions.

## Slide 5: CONSTRUCTION
Components used:
  BASIC STAMP 2 Microcontroller
  Parallax Standard Servomotor
  PIR ( Passive Infrared) Sensors
  Digital Potentiometer (AD5220)
  Transistor
  Temperature Sensor (DS1620)

## Slide 7
CIRCUIT LAYOUT

## Slide 8: CIRCUITS
PIR (Passive Infrared) Sensor
The PIR sensor will give a HIGH or LOW signal depending on whether it can detect motion or not.

## Slide 9
Standard Servomotor
Based on the sensor that detects the motion, the servo head, carrying the fan, is moved to that particular position

## Slide 10
Temperature Sensor (DS1620)
The output of the temperature sensor will indicate the ambient temperature.
The speed of the fan is varied accordingly with respect to the increase or decrease in the temperature.

## Slide 11
Digital Potentiometer (AD5220)
The potentiometer is used to vary the speed of the fan by varying the resistance
With every degree increase, the potentiometer is varies by 20 steps.

## Slide 12
Miscellaneous Circuits
  Bicolor LED
  Green – Increasing Temperature
  Red – Decreasing Temperature
  Brushless DC motor (Fan)
  The output of the digital potentiometer is used to run the fan and vary the speed depending on the change in temperature

## Slide 13
  Pushbuttons
  Start Switch -
  Used to switch the circuit on or to restart the circuit.
  Kill Switch-
Used to stops the motion of the servo.

## Slide 14: WORKING

## Slide 16: PROBLEMS FACED
Sensor Calibration
  Difficulty in positioning the PIR sensors on the board to eliminate superposition of their sensing range
  Overcome by designing a mechanical structure separating the three sensors

## Slide 17
Temperature sensitivity output
  No observable change in fan speed corresponding to varying temperature
  Solved by using an LED which shows the incorporation of temperature change on the fan speed

## Slide 18
BASIC STAMP CODE

## Slide 20
MAIN PROGRAM:

## Slide 22
SUBROUTINES:

## Slide 25: COST ANALYSIS
No. | Component | Quantity | Cost
1. | BASIC STAMP 2 Microcontroller | 1 | $106.00
2. | PIR (Passive Infrared) Sensor | 2 | $20.00
3. | PIR (Passive Infrared) Mini | 1 | $9.00
4. | Standard Parallax Servomotor | 1 | $11.00
5. | RadioShack Microfan | 1 | $10.00
6. | Temperature Sensor (DS1620) | 1 | $5.00
7. | Digital Potentiometer (AD5220) | 1 | $3.00
8. | Misc. (Pushbuttons, Transistor, Resistors, etc.) | - | $3.00
 |  | Total | $167.00
Approximate Mass Production Cost = $70.00

## Slide 26: FUTURE SCOPE
Increase the range by incorporating a field of operation
Increasing the precision by addition of multiple sensors
Integration of the fan into a home automation system

## Slide 27: Thank You.